Ms. Baker
OSHW Bluetooth Model Rocket Telemetry Board

Ideal Technical Specifications:

- Designed operating voltage: 2.7v-3.6v
- Maximum supported rocket acceleration of 16g
- Apogee tolerance of ±1m
- BLE support
- 1 16g accelerometer
- 1 axial accelerometer to determine orientation
- Stores 3D accelration from 1 accelerometer and 1 axial accelerometer, all with 10-16bit resolution(2 bytes per axis, 6 bytes total per unit of time, 6kbytes per second)
- 1khz update rate
- Minimum 60 seconds of flight time recording, 512kbytes on onboard fram(lower memory options, possible upgradablility?)

IC List:
- 1x ATTINY85V-10SUR attiny85 10mhz microcontroller
- 1x RN4871-I/RM140 rn4871 uart bluetooth/i2c interface
- 4x MR44V100AMAZAATL 128kb I2C f-ram chips
- 1x TC7WH08FK,LJ(CT AND gate for 3-wire UART
- 2x LIS3DHTR I2C accelerometer
- 1x I3G4250DTR I2C gyroscope
- 1x MCP121T-270E/TT reset IC