Ms. Baker
OSHW Bluetooth Model Rocket Telemetry Board

Ideal Technical Specifications:

- Designed operating voltage: 2.7v-3.6v
- Maximum supported rocket acceleration of 16g
- Apogee tolerance of ±100m
- BLE support
- 1 16g accelerometer
- 1 axial accelerometer to determine orientation
- Stores 3D accelration from 1 accelerometer and 1 axial accelerometer, all with 10-16bit resolution(2 bytes per axis, 6 bytes total per unit of time, 6kbytes per second)
- 1khz update rate
- Minimum 60 seconds of flight time recording, 512kbytes on onboard fram(lower memory options, possible upgradablility?)

IC List:
- 1x ATTINY85V-10SUR attiny85 10mhz microcontroller
- 1x RN4871-I/RM140 rn4871 uart bluetooth/i2c interface
- 4x MR44V100AMAZAATL 128kb I2C f-ram chips
- 1x TC7WH08FK,LJ(CT AND gate for 3-wire UART
- 2x LIS3DHTR I2C accelerometer
- 1x I3G4250DTR I2C gyroscope
- 1x MCP121T-270E/TT reset IC

Schematic block list:

- ISP header block
- Reset block
- Power block
- I2C pullup block
- LED block
- 10Mhz quartz crystal block
- ATTINY block
- RN4871 block
- 512kbyte ram block
- Watchdog gyroscope block
- High-precision gyroscope block
- Watchdog accelerometer block
- High-precision accelerometer block
- 3-wire to 4-wire UART conversion block

# Block Descriptions
## ISP Header Block:

Block Function:

The ISP header block describes the interface between an external programmer and the rest of the circuit, particularly the ATTINY along with power connections

Internal References:

J1 – ISP 6 pin programming jack, connects an external programmer to the needed data and power lines

External References:

- BATT+ - Positive voltage supply for the rest of the circuit, in this case J1 supplies 3.3v for programming
- ISP_MISO – Master-In Slave-Out, data line for communication between the programmer (master) and ATTINY (slave)
- ISP_MOSI – Master-Out Slave-In, data line for communication between the programmer (master) and ATTINY (slave)
- ISP_SCK – Serial ClocK, clock line for for communication between the programmer (master) and ATTINY (slave)
- RESET – IC reset line, in this case used to initiate programming with the ATTINY
- PGND – Programming GrouND, special ground connection between J1 and the ATTINY that can be seperated from the board-wide ground supply, so that no other ICs are active while programming
## Reset Block:

Block Function:

The reset block is in charge of keeping the RESET line on ICs low if the battery voltage is unstable/too low. Otherwise, it is in charge of keeping the reset line high in all other circumstances

Internal References:

- C1 – 10uF ceramic bypass capacitor placed closely to U1
- R1 – 10kΩ pull-up resistor for the RESET line
- U1 – MCP121T-270E_TT reset IC, pulls the RESET line low until the voltage has stayed above 2.6v for longer than 120ms

External References:

- BATT+ - Positive voltage supply
- GROUND – board-wide ground supply
- RESET – IC reset line, LOW resets all ICs connected to this line, the only exception being U1
## Power Block:

Block Function:

The function of the power block is very simple: provide 3v of DC power for the rest of the circuit

Internal References:

BT1 – 3v 1632 lithium coin cell

External References:

- BATT+ - Positive voltage supply, in this case the lithium cell is providing 3v to the rest of the devices connected to this line
- GROUND – board-wide ground supply
## I2C Pullup Block:

Block Function:

The I2C block provides pullup resistors for both the I2C clock line and the I2C data line

Internal References:

R2 & R3 – 2.2kΩ resistors that pull up the I2C SCL and SDA lines respectively, optimized for 10 maximum I2C devices on battery power

External References:

- BATT+ - Positive voltage supply, in this case the lithium cell is providing 3v to the rest of the devices connected to this line
- I2C_SCL – I2C serial clock line, provides all I2C devices with a clock
- I2C_SDA – I2C serial data line, bi-directional data line for all I2C devices
## Power Block:

Block Function:

The function of the power block is very simple: provide 3v of DC power for the rest of the circuit

Internal References:

BT1 – 3v 1632 lithium coin cell

External References:

- BATT+ - Positive voltage supply, in this case the lithium cell is providing 3v to the rest of the devices connected to this line
- GROUND – board-wide ground supply