Ms. Baker
OSHW Bluetooth Model Rocket Telemetry Board

Ideal Technical Specifications:

- Designed operating voltage: 2.7v-3.6v
- Maximum supported rocket acceleration of 16g
- Apogee tolerance of ±100m
- BLE support
- 1 16g accelerometer
- 1 axial accelerometer to determine orientation
- Stores 3D accelration from 1 accelerometer and 1 axial accelerometer, all with 10-16bit resolution(2 bytes per axis, 6 bytes total per unit of time, 6kbytes per second)
- 1khz update rate
- Minimum 60 seconds of flight time recording, 512kbytes on onboard fram(lower memory options, possible upgradablility?)

IC List:
- 1x ATTINY85V-10SUR attiny85 10mhz microcontroller
- 1x RN4871-I/RM140 rn4871 uart bluetooth/i2c interface
- 4x MR44V100AMAZAATL 128kb I2C f-ram chips
- 1x TC7WH08FK,LJ(CT AND gate for 3-wire UART
- 2x LIS3DHTR I2C accelerometer
- 1x I3G4250DTR I2C gyroscope
- 1x MCP121T-270E/TT reset IC

Schematic block list:

- ISP header block
- Reset block
- Power block
- I2C pullup block
- LED block
- 10Mhz quartz crystal block
- ATTINY block
- RN4871 block
- 512kbyte ram block
- Watchdog gyroscope block
- High-precision gyroscope block
- Watchdog accelerometer block
- High-precision accelerometer block
- 3-wire to 4-wire UART conversion block

# Block Descriptions
## ISP Header Block:

Block Function:

The ISP header block describes the interface between an external programmer and the rest of the circuit, particularly the ATTINY along with power connections

Internal References:

J1 – ISP 6 pin programming jack, connects an external programmer to the needed data and power lines

External References:

- BATT+ - Positive voltage supply for the rest of the circuit, in this case J1 supplies 3.3v for programming
- ISP_MISO – Master-In Slave-Out, data line for communication between the programmer (master) and ATTINY (slave)
- ISP_MOSI – Master-Out Slave-In, data line for communication between the programmer (master) and ATTINY (slave)
- ISP_SCK – Serial ClocK, clock line for for communication between the programmer (master) and ATTINY (slave)
- RESET – IC reset line, in this case used to initiate programming with the ATTINY
- PGND – Programming GrouND, special ground connection between J1 and the ATTINY that can be seperated from the board-wide ground supply, so that no other ICs are active while programming
## Reset Block:

Block Function:

The reset block is in charge of keeping the RESET line on ICs low if the battery voltage is unstable/too low. Otherwise, it is in charge of keeping the reset line high in all other circumstances

Internal References:

- C1 – 10uF ceramic bypass capacitor placed closely to U1
- R1 – 10kΩ pull-up resistor for the RESET line
- U1 – MCP121T-270E_TT reset IC, pulls the RESET line low until the voltage has stayed above 2.6v for longer than 120ms

External References:

- BATT+ - Positive voltage supply
- GROUND – board-wide ground supply
- RESET – IC reset line, LOW resets all ICs connected to this line, the only exception being U1
## Power Block:

Block Function:

The function of the power block is very simple: provide 3v of DC power for the rest of the circuit

Internal References:

BT1 – 3v 1632 lithium coin cell

External References:

- BATT+ - Positive voltage supply, in this case the lithium cell is providing 3v to the rest of the devices connected to this line
- GROUND – board-wide ground supply
## I2C Pullup Block:

Block Function:

The I2C block provides pullup resistors for both the I2C clock line and the I2C data line

Internal References:

R2 & R3 – 2.2kΩ resistors that pull up the I2C SCL and SDA lines respectively, optimized for 10 maximum I2C devices on battery power

External References:

- BATT+ - Positive voltage supply
- I2C_SCL – I2C serial clock line, provides all I2C devices with a clock
- I2C_SDA – I2C serial data line, bi-directional data line for all I2C devices
## LED Block:

Block Function:

The LED block provides indication LEDs for various lines across the board

Internal References:

- D1 – Blue LED diode, rated minimum 10mA
- R4 – 680Ω current limiting resistor, limits the LED current to less than 5mA at 3.3v

External References:

- BATT+ - Positive voltage supply
- GROUND – board-wide ground supply
- LED_BTON – Line from the RN4871 to an indicator LED; is powered when the RN4871 is active

## 10MHZ Quartz Crystal Block:

Block Function:

The quartz crystal block provides the components necissary for the ATTINY to run on an external 10MHz quartz crystal

Internal References:

- Y1 – 10MHZ quartz crystal
- C8 & C9 – 22pF ceramic capacitors necissary for crystal oscillation

External References:

- BATT+ - Positive voltage supply
- CLKI – ATTINY clock input
- CLKO – ATTINY clock output
- GROUND – board-wide ground supply

## ATTINY Block:

Block Function:

The ATTINY block consists of an ATTINY85-10mhz microcontroller along with bypass capacitor and other etc’s.

The clock is generated by a 10mhz quartz crystal along pins CLKI and CLKO.

When programming, the ATTINY’s ground can be disconnected from the rest of the board so the programming data lines do not interfere with other ICs

The ATTINY85 ultimately controls the RN4871 via a 115200 baud UART connection. A single pin is used for both RX and TX: whether it is RX or TX is dependent on the state of the RTS/CTS lines. When RN4871_RTS

Internal References:

- U4 – ATTINY85
- C10 – 10uF ceramic bypass capacitor
- JP1 – Physical jumper that disconnects the ATTINY’s programming ground from the board-wide ground supply, to prevent any other chips from misinterpreting the programming signals

External References:

- ATTINY_RTS – Request To Send, pulled high if the ATTINY is ready to recieve data
- ATTINY_UART – RX/TX pin for UART communications
- BATT+ - Positive voltage supply
- CLKI – ATTINY clock input
- CLKO – ATTINY clock output
- GROUND – board-wide ground supply
- RESET - IC reset line, LOW resets all ICs connected to this line, the only exception being U1
- RN4871_RTS – Request To Sent, pulled high if the RN4871 is ready to receive data
- PGND – Programming GrouND, special ground connection between J1 and the ATTINY that can be seperated from the board-wide ground supply, so that no other ICs are active while programming