Ms. Baker Schematic Checklist
Schematic Revision 2.3
Write component ids under the bullet point, if applicable
# ESP32 BLOCK
- 100nF capacitors connecting esp32/pins 19 and 37 respectively to ground
- esp32/pins 19 and 37 connected to V3.3+
- 1uF capacitor connecting esp32/pin 26 to ground
- 100nF, 1uF, and 10uF capacitors connecting both esp32/pins 3 and 4 to ground
- 2nH inductor connecting both esp32/pins 3 and 4 to the aformentioned bypass capacitors
- both esp32/pins 3 and 4 connected to V3.3+
- 100pF and 1uF capacitors connecting both esp32/pins 46 and 43 to ground
- both esp32/pins 46 and 43 connected to V3.3+
- 100nF capacitor connecting esp32/pin 1 to ground
- esp32/pin 1 connected to V3.3+
- esp32/pin 9 connected to reset
- 10nF capacitor connecting esp32/pin48 to ground
- 499ohm resistor connecting esp32/pin 41 to UART_TX
- esp32/pin 25 connected to SPI_CS
- esp32/pin 27 connected to SPI_IO1
- esp32/pin 30 connected to SPI_IO3
- esp32/pin 31 connected to SPI_CLK
- esp32/pin 32 connected to SPI_IO2
- esp32/pin 33 connected to SPI_IO0
- esp32/pin 14 connected to I2C_SCK
- esp32/pin 15 connected to I2C_SDA
- esp32/pin 23 connected to BOOTMODE
- esp32/pin 40 connected to UART_RX
- esp32/pin 34 connected to the BT STATUS LED
- esp32/pin 35 connected to the BOOT STATUS LED
- esp32/pin 36 connected to the ERROR LED
- esp32/pin 17 connected to JTAG_MTMS
- esp32/pin 18 connected to JTAG_MTDI
- esp32/pin 20 connected to JTAG_MTCK
- esp32/pin 21 connected to JTAG_MTDO
# CPU CRYSTAL BLOCK
- 40MHz crystal connected between esp32/pins 44 and 45
- 0ohm resistor in series between esp32/pin 45 and the 40MHz crystal
- 12pF capacitors connected to both 40MHz/pins 1 and 3 respectively
- 40MHz/pins 2 and 4 connected to ground
# RTC CRYSTAL BLOCK
- 32.768kHz crystal connected between esp32/pins 12 and 13
- 12pF capacitors connected to both 32.768kHz/pins 1 and 2 respectively
# RESET BLOCK
- 100nF capacitor connecting mcp130/pin 2 to ground
- jumper connecting mcp130/pin1 to reset
- mcp130/pin 2 connected to V3.3+
- mcp130/pin 3 connected to ground
# ANTENNA BLOCK
- One inductor and two capacitors configured in pi-style matching network
- Use center-tapped inductor or two inductors for tuning
# I2C PULLUP BLOCK
2 12kOhm resistors connecting I2C_SCK and I2C_SDA respectively to V3.3+
# LED BLOCK
- 120Ohm resistor between each LED and their respective esp32 pin
- 2.1v LEDs
- BLUE=BLUETOOTH, GREEN=STATUS, RED=ERROR
# POWER SUPPLY BLOCK
- 10uF capacitor connecting adp124/pins 7 and 8 to ground
- 10uF capacitor connecting adp124/pins 1 and 2 to ground
- 1uF capacitor connecting adp150/pin 1 to ground
- 1uF capacitor connecting adp150/pin 5 to ground
- adp124/pins 5, 7 and 8 connected to a 3.7v LiPo battery, preferably via a Molex Picoblade
- adp124/pins 1, 2, and 3 connected to V3.3+
- adp124/pin 4 connected to ground
- adp150/pins 1 and 3 connected to V3.3+
- adp150/pin 2 connected to ground
- adp150/pin 5 connected to V1.8+
# IMU BLOCK
- 100nF and 2.2uF capacitor connecting icm20601/pin 16 to ground
- 10nF capacitor connecting icm20601/pin 1 to ground
- 470nF capacitor connecting icm20601/pin 14 to ground
- icm20601/pin 1 connected to V3.3+
- icm20601/pin 2 connected to I2C_SCK
- icm20601/pin 3 connected to I2C_SDA
- icm20601/pin 4 connected to ground
- icm20601/pin 5 connected to V3.3+
- icm20601/pin 8 connected to ground
- icm20601/pin 13 connected to ground
- icm20601/pin 16 connected to V1.8V+
# FERAM BLOCK
- 2.2uF capacitor connecting fm24v01/pin 8 to ground
- fm24v01/pins 1, 2, and 3 connected to ground
- fm24v01/pin 4 connected to ground
- fm24v01/pin 5 connected to I2C_SDA
- fm24v01/pin 6 connected to I2C_SCK
- fm24v01/pin 7 connected to ground
- fm24v01/pin 8 connected to V3.3+